# MEMO

| To: | Don Schultz, CPUC/ORA |
| --- | --- |
| From: | Kenneth M. Keating, ORA Evaluation Consultant |
| Date: | July 30, 1998 |
| Subject: | Review Memo for SCE Study # 540: CEEI Lighting and HVAC |

# REVIEW SUMMARY

1. Utility:  Southern California Edison                        			Study ID: 540

Program and PY:  Commercial Energy Efficiency Incentives Program: PY1996

# End Use(s):  lighting;  HVAC

2.  Utility Study Title:  “1996 Commercial Energy Management Hardware Rebate Program Impact Evaluation”

3. Type of Study:  1st Year Load Impact Study                		 Required by Table 8A: Yes.

# 4. Applicable Protocols: Tables 5, 6, 7, and C-4.

Study Completion:  February 27, 1998 	Required Documentation Received:   Yes

Retroactive Waivers:   None

# 5.  Reported Impact Results;

# Average Annual Gross Load Impacts:

Lighting:  Peak: 4,392 kW (0.00008 per designated unit;  0.96 realization rate). Energy: 20,769,622 kWh (0.3857 kWh per designated unit;  0.808 realization rate).

HVAC:  Peak: 1,785  kW (0.00003 kW per designated unit; 2.61 realization rate).   Energy:  13,950,105 kWh (0.2721 kWh per designated unit; 0.664 realization rate).

# Average Annual  Net Load Impacts:

Lighting; Peak:  3,460  kW (0.00006 per designated unit; 1.06 realization rate).  Energy:  16,131,726 kWh (0.2995 kWh per designated unit;  0.9126 realization rate)

HVAC:  Peak:  1,649 kW (0.00003 kW per designated unit; 2.93 realization rate).  Energy: 12,886,960 kWh (0.2463 kWh per designated unit; 0.7536 realization rate )

Net-to-gross ratios:  	 0.79 for peak lighting		0.92 for peak HVAC

.	 0.78 for kWh lighting		0.92 for kWh HVAC

# 7.  Review Findings:

- Conformity with Protocols:  The study is generally in conformity with the protocols.

- Acceptability of Study results: This very important study clearly needs a Verification Report.

Recommendations:  Pending a Verification Report, the recommendation is to revise the NTG ratios to those ratios found in Table 5-1 of the Study.  This will result in an increase in the net load impacts that resulted from this program evaluation, because the NTG for the indoor lighting end-use is more properly 0.95 and for the HVAC end-use, 0.989.

.

# OVERVIEW

The Commercial Energy Efficiency Incentives Program is a shared savings program for purposes of shareholder incentives.  As such, the actual ex post evaluation results from the first year load impact study are important to the calculation of that shareholder incentive.  Approximately 36% of the Company’s claimed net benefits for all shared saving programs are based on the CEEI, and of that, 96% is due to the Lighting and HVAC end uses.   However, much of the CEEI net benefits in the first earnings claim were based on the projected load impacts from the DSM bidding pilot (49%), which load impacts are the subject of Study 539.   The results of this Study  (#540) are worth approximately $2.9 million in share holder incentives. Therefore, the load impact study will be carefully reviewed through a Review Memo and replicated  with a Verification Report.

# REPORTED IMPACT RESULTS:

Based the revised Table 6 found in the Attachment B to this Review Memo, the following claims were made for load impacts:

# Average Annual Gross Load Impacts:

Lighting:  Peak: 4,392 kW (0.00008 per designated unit;  0.96 realization rate). Energy: 20,769,622 kWh (0.3857 kWh per designated unit;  0.808 realization rate).

HVAC:  Peak: 1,785  kW (0.00003 kW per designated unit; 2.61 realization rate).   Energy:  13,950,105 kWh (0.2721 kWh per designated unit; 0.664 realization rate).

# Average Annual  Net Load Impacts:

Lighting; Peak:  3,460  kW (0.00006 per designated unit; 1.06 realization rate).  Energy:  16,131,726 kWh (0.2995 kWh per designated unit;  0.9126 realization rate)

HVAC:  Peak:  1,649 kW (0.00003 kW per designated unit; 2.93 realization rate).  Energy: 12,886,960 kWh (0.2463 kWh per designated unit; 0.7536 realization rate )

Net-to-gross ratios:  	 0.79 for peak lighting		0.92 for peak HVAC

.	 0.78 for kWh lighting		0.92 for kWh HVAC

# ASSESSMENT OF STUDY METHODOLOGY AND RESULTS

This is a very carefully done and rigorously documented study. Any simple description of the techniques employed and adjustments made will not do justice to the sophistication of the study.   Given that caveat, this is a multi-stage study that began with new engineering estimates computed via on-site visits to a modified census of participants (269) and 305 matched nonparticipants.  The revised engineering estimates of expected load impacts from both program-eligible and program-ineligible measures in participants and nonparticipant facilities were used as engineering priors in a “realization rate model.”  This model uses monthly data in a load impact regression model (LIRM), pooling both participants and the comparison group of non-participants to determine how closely the billing data reflect the expected load impacts from the engineering priors.

Several adjustments are necessary to weather-normalize the results, to adjust for Title-24 requirements instead of the pre-existing condition reflected in the pre-retrofit bills, and to “levelize” the stream of expected savings.

The net-to-gross ratios are computed for each end-use element through a very literal “difference-of-differences” approach that compares the load reduction the participants attained over the first year with those attained by the nonparticipants.  Then these  NTG ratios are adjusted to reflect an assumption that in each year after the program participation, the same fraction of participants would have similarly chosen to take measures outside of the program, as reflected in the behavior of the nonparticipants in the first year load impact study.  This in  a sense results in a  “compounded” net-to-gross ratio that is substantially below the first year estimate.

# EVALUATION ISSUES:

Two minor issues remain, and one major issue, arise from the review of this Study.  The apparently minor issues include:

# Was it really appropriate to do the analyses on the full life of the measures, and did it make any difference?

# And how valid was it to assume that the Title-24 based load impacts were appropriate for one-half the measure life, and the load impacts based on the pre-retrofit conditions  were appropriate for the other half of the measure life – and how big a difference does that make?

# The major issue was the decision to discount the net-to-gross ratio.

### Minor Issues

# Was it really appropriate to do the analyses on the full life of the measures, and did it make any difference?

# The gross load impacts were “developed based on the useful life of each measure, customer (pre-participation baseline) and reportable (Title 24 baseline) savings. This stream of savings was then collapsed to its present value and used to calculate a constant annual savings amount.  This constant or levelized annual savings is the estimated “gross savings.”  (Page 4-14).  Given that there was a correction factor included to get from “customer savings” to “reportable savings,” and the fact that the utility’s feeder Tables should already account for the differing measure lives, this may be an over-correction.  It is certainly the first time in the AEAP process that this type of levelized load impacts have been generated by the study authors.  The Verification Report should probably test the alternative decision to simply use the adjusted gross load impacts.

# How valid was it to assume that the Title-24 based load impacts were appropriate for one-half the measure life, and the load impacts based on the pre-retrofit conditions  were appropriate for the other half of the measure life – and how big a difference does that make?

# This is related to the last issue and is found in footnote 6  on Page 4-14.  Perhaps this arbitrary decision (approximation) mutes the effect of the decision to levelize gross load impacts, but this isn’t clear, and some examination of the sensitivity of the results to this decision might be considered in the Verification Report.

# Major Issue

# On page 5-3, the authors describe the method used to adjust first year NTG to get to what they call an overall net-to-gross ratio, basically by compounding the estimate of naturally occurring conservation (which is what is picked up in the “difference of differences” approach to net load impacts) over the expected lives of the measures.  The argument presented is that a fraction of the participants would have been faced with “the decision of whether or not to retrofit their existing equipment had they not entered the program” each of the remaining years of the life of the measures.  On page 4-14, the authors note that 97% of the program activity was for retrofits.  While it is true that if an HVAC system failed completely, it would have to be replaced with Title-24 compliant equipment, at least a portion of the participants would have repaired the old equipment.  And they wouldn’t have necessarily gone above Title 24 to the level of the program efficiencies.  On the other hand, the participants who were retrofitting lighting equipment in 1996 could have chosen, in the absence of a program, to continue replacing failed bulbs and ballasts with like equipment indefinitely.  This would be different if we were talking about a program designed to intervene in a renovation, build out, or remodel, but a retrofitting participant is under no compunction to act in the out years.

# It can be argued that the “difference of differences” approach to net load impacts does not account for the self-selection among participants, and therefore reflects an inflated net program effect.  However, self-selection only reflects a tendency to act, and the incentive may be necessary to convince the participants to act on their tendency. On the other hand, the approach will always count any spillover in the nonparticipants as an indication of naturally-occurring conservation.  Therefore, the “difference of differences” approach can not be argued to be so biased in either direction to justify the type of discounting-through -compounding applied in this case.

# CONFORMITY WITH THE PROTOCOLS

Measurement Protocols.  The study  is in general conformity to the Protocols of Table C-4 and Table 5.

Tables 6 and 7 Reporting Protocols.   The Study is in conformity with the requirements for Table 6 (as revised in Attachment B to this Review Memo), and Table 7 is adequate, although, by repeatedly referencing extended portions of the text instead of concisely summarizing what was done in the Study and why it was done, the authors defeat the purpose of the summary reporting Tables.

# Summary Recommendation:

The importance of this evaluation requires a Verification Report. In the absence of a Verification Report, the sole recommendation is to replace the Study’s NTG ratios, based on “compounded” free-ridership, with those in Table 5-1.  This, at the simplest level, results in an increase in the net load impacts for lighting kWh from 16,131,726 kWh to 19,793,450 kWh (an increase of 3,661,724 kWh) and kW from 3,460 to 4,186 (an increase of 726 kW).

For HVAC, the revised kWh would be 13,796,654 instead of 12,886,960 (an increase of 909,694 kWh); for peak the increase is approximately 116 kW.

# ATTACHMENTS

## Attachment A

To: 	Marian Brown  [April 11, 1998]

Re: 	Data Request

I find that it is difficult to make sense of the Table 6 filed in the Study and the E-3 Table filed 10/28/97 (revised).

I have difficulty moving ahead on this review memo (Issues listed in 1st draft of RM):

- Table 6 does not break out the load impacts by the end-use elements. Are the Miscellaneous measures in fact, not miscellaneous (less than 15% of resource value and estimated in the first earnings claim), and require a separate load impact study as included in Study 540?

- The proper designated unit for lighting is kW/sq-1000hrs of operation.  This Study does not follow that designation, using instead kW (and kWh) per sq. ft.   Has SCE received retroactive waivers concerning DUs or combining end-use elements?

- The text and Table 6 of the Study do not appear to be related to the E-3 Table for CEEI for Edison, at least not the version revised on 10/28/97. Has SCE filed more recent and usable E-3 Tables?  For example, the net realization rate reported for kWh across all end-use elements in Table 6 is 0.798, but dividing the reported total net load impacts reported in Table 6 for all end-use elements, by the total net impacts claimed across all end-use elements in the 10/28/97 E-3 Table results in a net realization rate of 0.424.

- The NTG reported does not appear to make sense, as the E-3 Table NTG for lighting was 0.86, and the NTG  is 0.77, from Table 6.  If the gross is less than the E-3 Table (or the ex ante shown in Table 2 of the Study, since there seems to be a disconnect between the Study and the E-3 Tables) and the net is less than the gross as shown in Table 6, and the difference is not explained by a much lower NTG in the E-3 table, then the net realization rate should be less than 1.0.

# Attachment B

Response from SCE on Data Request:  [April 14, 1998]

# Question No. 1:

Table 6 does not break out the load impacts by the end-use elements.

# Response To Question No. 1:

These rows were omitted in error and appear in the revised version of Table 6 in Attachment A of this response.

In addition, in the process of preparing the 1998 AEAP earnings claim based on this study, a misclassification of measures was discovered and is corrected in the revised version of Table 6 in Attachment A of this response.  These measures were originally misclassified in last year’s initial earnings claim for the 1996 Energy Efficiency Incentive (EEI) program because in the forecast for the 1996 program, the E-Tables for commercial end uses did not include a miscellaneous category.  When the program was implemented, two measures were installed that were not forecasted: adjustable speed drives were attached to water pumps at two sewage services.  This is usually a measure reported in the Agriculture/Water Services sector, but the sites were properly classified as Commercial.

Because there was no “water pumping” measure for them in the forecast, in the 1997 AEAP’s earnings application they were combined with the most similar forecasted measure: Customized HVAC.  In negotiations with the ORA, Edison did revise its estimated savings (as reflected in the revised E-tables filed in November 1997 and cited in Decision 98-03-063), but no changes were made in the classification of these two measures.

In the impact analysis of Edison’s 1996 EEI program for commercial customers (Study 540, filed March 2, 1998), the two ASDs were initially grouped in the HVAC end-use category.  However, while the results of that study were being used to update the E-tables in preparation for the 1998 AEAP application filing on May 1, 1998, we decided to correct the earlier misclassification, since the impact analyses are intended to be a “truing-up” of the initial earnings claim.  The changes involved moving the two ASD measures from the HVAC end use to the Miscellaneous end-use.  The savings estimates change slightly because of different default NTGRs, etc.  Corrections were also made to several intermediate tables in the body of Study 540 (also attached).

# Prepared By:	Pierre Landry

Title:	Project Manager, Measurement and Evaluation

Question No. 2:

The proper designated unit for lighting is kW/sq-1000 hrs of operation.  This Study does not follow that designation, using instead kW (and kWh) per sq. ft.

# Response To Question No. 2:

The correct units were used in the calculations, but the row label in Table 6 is incorrect.  The correct units appear in the revised version of Table 6 in Attachment A of this response.

# Prepared By:	Pierre Landry

Title:	Project Manager, Measurement and Evaluation

# Question No. 3:

The text and Table 6 of the Study do not appear to be related to the E-3 Table for CEEI for Edison, at least not the version revised on 10/28/97.  For example, the net realization rate reported for kWh across all end-use elements in Table 6 is 0.798, but dividing the reported total net load impacts reported in Table 6 for all end-use elements, by the total net impacts claimed across all end-use elements in the 10/28/97 E-3 Table results in a net realization rate of 0.424.

# Response To Question No. 3:

The reason for this apparent discrepancy stems from the ORA requirement that the utilities file E-tables for program categories – in this case, “Commercial Energy Efficiency Incentive [CEEI] Programs.”  The November 1997 E-tables for CEEI programs mentioned by Mr. Keating represent the combined results of (a) Edison’s 1996 “DSM Pilot Bidding Program”, and (b) commercial-customer participation in Edison’s 1996 “Energy Efficiency Incentive Program” (formerly called the “Energy Management Hardware Rebate Program”).  Mr. Keating is comparing the results from Study 540 (which studied just the commercial participants in our EEI program) with the combined results of both commercial incentive programs.  Table 1 (below) compares the derivations of the two numbers cited by Mr. Keating.

| Table 1. Derivation of Two Realization Rates Cited in Question 3. |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Extract From Table E-3 (Commercial EEI & DSM Bidding Pilot) |  |  |  |  |  | Feeder Sheets for E-3 |  |
| EndUse | Avg kWh / Unit | x # Units | x NTGR | = net kWh impacts |  | (Comm. EEI only) |  |
| LTG | 0.47 | 109,747,873 | 0.86 | 44,360,090.27 |  | 17,677,140.26 |  |
| MISC | 315,582.82 | 13 | 0.80 | 3,282,061.33 |  | 3,282,061.33 |  |
| SPCOND | 0.44 | 77,127,323 | 0.95 | 32,239,221.01 |  | 21,469,501.42 |  |
|  |  | 10/28/97 | ==> | 79,881,372.61 | (a) | 42,428,703.02 | (c) |
|  |  | Study 540(3/98)==> |  | 33,875,176.00 | (b) | 33,875,176.00 | (d) |
|  |  | Realization Rate ==> |  | 0.4241 | (b/a) | 0.7984 | (d/c) |
| (a) | total net kWh impacts, as calculated by KK from Table E-3 (10/28/97 negotiated version) |  |  |  |  |  |  |
| (b) | total net kWh impacts, as report in Study 540, Table 6, row 2.A.ii (3/2/98) |  |  |  |  |  |  |
| (c) | total net kWh impacts, as calculated from feeder sheets ("Table C") for Table E-3 (10/28/97 negotiated version) for Energy Efficiency Incentive Program only (without DSM Bidding Pilot results) |  |  |  |  |  |  |
| (d) | = (b) |  |  |  |  |  |  |

Prepared By:	Pierre Landry

Title:	Project Manager, Measurement and Evaluation

# ATTACHMENTS TO LANDRY MEMO

| SCE Impacts Per Designated Unit of Measure |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | kW |  | SCE Savings - Gross | SCE Savings-Net | DUs | unit | SCE Savings/Unit - Gross | SCE Savings/Unit - Net | Reference |
|  |  | Lighting | 4573 | 3260 | 53,855,143 | kW/sqft/kOpHrs | 0.00008491 | 0.00006053 | SCE's Filings |
|  |  | HVAC | 685 | 563 | 54,625,715 | kW/sqft | 0.00001254 | 0.00001031 | SCE's Filings |
|  |  | Miscellaneous | 196 | 155 | 15 | kW/project | 13.06666667 | 10.33333333 |  |
|  |  | Miscellaneous includes process + refrigeration + 2 water sites |  |  |  |  |  |  |  |
|  |  | HVAC = HVAC |  |  |  |  |  |  |  |
|  | kWh |  | SCE Savings - Gross | SCE Savings-Net | DUs | unit | SCE Savings/Unit - Gross | SCE Savings/Unit - Net | Reference |
|  |  | Lighting | 25,701,277 | 17,677,140 | 53,855,143 | kWh/sqft/kOpHrs | 0.47722976 | 0.32823495 | SCE's Filings |
|  |  | HVAC | 24,670,308 | 19,590,103 | 54,625,715 | kWh/sqft | 0.45162444 | 0.35862420 | SCE's Filings |
|  |  | Miscellaneous | 6,654,143 | 5,161,460 | 15 | kWh/project | 443609.53333333 | 344097.33333333 |  |
|  |  | Miscellaneous includes process, and refrigeration + 2 water sites |  |  |  |  |  |  |  |
|  |  | HVAC = HVAC |  |  |  |  |  |  |  |

| Southern California Edison |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M&E PROTOCOLS TABLE 6 - RESULTS USED TO SUPPORT PY96 SECOND EARNINGS CLAIM FOR THE COMMERCIAL ENERGY MANAGEMENT HARDWARE REBATE PROGRAM |  |  |  |  |  |  |  |  |  |  |  |
| FIRST YEAR LOAD IMPACT EVALUATION, FEBRUARY 1998, STUDY ID NO. 540 |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | 5. A. 90% CONFIDENCE LEVEL |  |  |  | 5. B. 80% CONFIDENCE LEVEL |  |  |  |
|  |  |  |  | LOWER BOUND | UPPER BOUND | LOWER BOUND | UPPER BOUND | LOWER BOUND | UPPER BOUND | LOWER BOUND | UPPER BOUND |
| 1. Average Participant Group and Average Comparison Group |  | PART GRP | COMP GRP | PART GRP | PART GRP | COMP GRP | COMP GRP | PART GRP | PART GRP | COMP GRP | COMP GRP |
| A. Pre-install usage: | Pre-install kW | na | na | na | na | na | na | na | na | na | na |
|  | Pre-install kWh | na | na | na | na | na | na | na | na | na | na |
|  | Base kW | na | na | na | na | na | na | na | na | na | na |
|  | Base kWh | na | na | na | na | na | na | na | na | na | na |
|  | Base kW/ designated unit of measurement | na | na | na | na | na | na | na | na | na | na |
|  | Base kWh/ designated unit of measurement | na | na | na | na | na | na | na | na | na | na |
| B. Impact year usage: | Impact Yr kW | na | na | na | na | na | na | na | na | na | na |
|  | Impact Yr kWh | na | na | na | na | na | na | na | na | na | na |
|  | Impact Yr kW/designated unit | na | na | na | na | na | na | na | na | na | na |
|  | Impact Yr kWh/designated unit | na | na | na | na | na | na | na | na | na | na |
| 2. Average Net and Gross End Use Load Impacts |  | AVG GROSS | AVG NET | AVG GROSS | AVG GROSS | AVG NET | AVG NET | AVG GROSS | AVG GROSS | AVG NET | AVG NET |
|  | A. i. Load Impacts - kW | 6,605 | 5,510 | 6,094 | 7,116 | 5,084 | 5,936 | 6,207 | 7,003 | 5,178 | 5,842 |
|  | Lighting | 4,392 | 3,460 | 4,010 | 4,774 | 3,159 | 3,761 | 4,094 | 4,690 | 3,225 | 3,695 |
|  | HVAC | 1,785 | 1,649 | 1,478 | 2,092 | 1,365 | 1,933 | 1,546 | 2,024 | 1,428 | 1,870 |
|  | Miscellaneous | 428 | 401 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
|  | A. ii. Load Impacts - kWh | 40,307,432 | 33,875,176 | 37,191,063 | 43,423,801 | 31,256,117 | 36,494,235 | 37,878,748 | 42,736,116 | 31,834,061 | 35,916,291 |
|  | Lighting | 20,769,622 | 16,131,726 | 18,962,925 | 22,576,319 | 14,728,468 | 17,534,984 | 19,361,606 | 22,177,638 | 15,038,123 | 17,225,329 |
|  | HVAC | 13,950,105 | 12,886,960 | 11,551,733 | 16,348,477 | 10,671,369 | 15,102,551 | 12,080,979 | 15,819,231 | 11,160,281 | 14,613,639 |
|  | Miscellaneous | 5,587,706 | 4,856,490 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
|  | B. i. Load Impacts/designated unit - kW |  |  |  |  |  |  |  |  |  |  |
|  | Lighting (kW/sqft/1,000 hrs of operation) | 0.00008155 | 0.00006425 | 0.00007446 | 0.00008865 | 0.00005866 | 0.00006984 | 0.00007602 | 0.00008708 | 0.00005989 | 0.00006860 |
|  | HVAC (kW/sqft) | 0.00003268 | 0.00003019 | 0.00002706 | 0.00003829 | 0.00002500 | 0.00003538 | 0.00002830 | 0.00003706 | 0.00002614 | 0.00003423 |
|  | Miscellaneous (kW/project) | 28.5333 | 26.7333 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
|  | B. ii. Load Impacts/designated unit - kWh |  |  |  |  |  |  |  |  |  |  |
|  | Lighting (kWh/sqft/1,000 hrs of operation) | 0.3857 | 0.2995 | 0.3521 | 0.4192 | 0.2735 | 0.3256 | 0.3595 | 0.4118 | 0.2792 | 0.3198 |
|  | HVAC (kWh/sqft) | 0.2554 | 0.2359 | 0.2115 | 0.2993 | 0.1954 | 0.2765 | 0.2212 | 0.2896 | 0.2043 | 0.2675 |
|  | Miscellaneous (kWh/project) | 372,514 | 323,766 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
|  | C. i. a. % change in usage - Part Grp - kW | na | na | na | na | na | na | na | na | na | na |
|  | C. i. b. % change in usage - Part Grp - kWh | na | na | na | na | na | na | na | na | na | na |
|  | C. ii. a. % change in usage - Comp Grp - kW | na | na | na | na | na | na | na | na | na | na |
|  | C. ii. b. % change in usage - Comp Grp - kWh | na | na | na | na | na | na | na | na | na | na |
| D. Realization Rate: | D.A. i. Load Impacts - kW, realization rate | 1.2113 | 1.3851 | 1.1176 | 1.3049 | 1.2780 | 1.4922 | 1.1383 | 1.2842 | 1.3017 | 1.4686 |
|  | Lighting | 0.9604 | 1.0613 | 0.8769 | 1.0440 | 0.9690 | 1.1537 | 0.8953 | 1.0255 | 0.9894 | 1.1333 |
|  | HVAC | 2.6058 | 2.9290 | 2.1578 | 3.0538 | 2.4254 | 3.4325 | 2.2567 | 2.9550 | 2.5365 | 3.3214 |
|  | Miscellaneous | 2.1837 | 2.5871 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
|  | D.A. ii. Load Impacts - kWh, realization rate | 0.7068 | 0.7984 | 0.6522 | 0.7615 | 0.7367 | 0.8601 | 0.6642 | 0.7494 | 0.7503 | 0.8465 |
|  | Lighting | 0.8081 | 0.9126 | 0.7378 | 0.8784 | 0.8332 | 0.9920 | 0.7533 | 0.8629 | 0.8507 | 0.9744 |
|  | HVAC | 0.5655 | 0.6578 | 0.4682 | 0.6627 | 0.5447 | 0.7709 | 0.4897 | 0.6412 | 0.5697 | 0.7460 |
|  | Miscellaneous | 0.8397 | 0.9409 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
|  | D.B. i. Load Impacts/designated unit - kW, real rate |  |  |  |  |  |  |  |  |  |  |
|  | Lighting | 0.9604 | 1.0613 | 0.8769 | 1.0440 | 0.9690 | 1.1537 | 0.8953 | 1.0255 | 0.9894 | 1.1333 |
|  | HVAC | 2.6058 | 2.9290 | 2.1578 | 3.0538 | 2.4254 | 3.4325 | 2.2567 | 2.9550 | 2.5365 | 3.3214 |
|  | Miscellaneous | 2.1837 | 2.5871 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
|  | D.B. ii. Load Impacts/designated unit - kWh, real rate |  |  |  |  |  |  |  |  |  |  |
|  | Lighting | 0.8081 | 0.9126 | 0.7378 | 0.8784 | 0.8332 | 0.9920 | 0.7533 | 0.8629 | 0.8507 | 0.9744 |
|  | HVAC | 0.5655 | 0.6578 | 0.4682 | 0.6627 | 0.5447 | 0.7709 | 0.4897 | 0.6412 | 0.5697 | 0.7460 |
|  | Miscellaneous | 0.8397 | 0.9409 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
| 3. Net-to-Gross Ratios |  | RATIO |  | RATIO | RATIO |  |  | RATIO | RATIO |  |  |
|  | A. i. Average Load Impacts - kW | 0.834 |  | 0.770 | 0.899 |  |  | 0.784 | 0.884 |  |  |
|  | Lighting | 0.788 |  | 0.719 | 0.856 |  |  | 0.734 | 0.841 |  |  |
|  | HVAC | 0.924 |  | 0.765 | 1.083 |  |  | 0.800 | 1.048 |  |  |
|  | Miscellaneous | 0.937 |  | n/a | n/a |  |  | n/a | n/a |  |  |
|  | A. ii. Average Load Impacts - kWh | 0.840 |  | 0.775 | 0.905 |  |  | 0.790 | 0.891 |  |  |
|  | Lighting | 0.777 |  | 0.709 | 0.844 |  |  | 0.724 | 0.829 |  |  |
|  | HVAC | 0.924 |  | 0.765 | 1.083 |  |  | 0.800 | 1.048 |  |  |
|  | Miscellaneous | 0.869 |  | n/a | n/a |  |  | n/a | n/a |  |  |
|  | B. i. Avg Load Impacts/designated unit of measurement - kW |  |  |  |  |  |  |  |  |  |  |
|  | Lighting | 0.788 |  | 0.719 | 0.856 |  |  | 0.734 | 0.841 |  |  |
|  | HVAC | 0.924 |  | 0.765 | 1.083 |  |  | 0.800 | 1.048 |  |  |
|  | Miscellaneous | 0.937 |  | n/a | n/a |  |  | n/a | n/a |  |  |
|  | B. ii. Avg Load Impacts/designated unit of measurement - kWh |  |  |  |  |  |  |  |  |  |  |
|  | Lighting | 0.777 |  | 0.709 | 0.844 |  |  | 0.724 | 0.829 |  |  |
|  | HVAC | 0.924 |  | 0.765 | 1.083 |  |  | 0.800 | 1.048 |  |  |
|  | Miscellaneous | 0.869 |  | n/a | n/a |  |  | n/a | n/a |  |  |
|  | C. i. Avg Load Impacts based on % chg in usage in Impact year relative to Base usage in Impact year - kW | na |  | na | na |  |  | na | na |  |  |
|  | C. ii. Avg Load Impacts based on % chg in usage in Impact year relative to Base usage in Impact year - kWh | na |  | na | na |  |  | na | na |  |  |
| 4. Designated Unit Intermediate Data |  | PART GRP | COMP GRP | PART GRP | PART GRP | COMP GRP | COMP GRP | PART GRP | PART GRP | COMP GRP | COMP GRP |
|  | A. Pre-install average value | na | na | na | na | na | na | na | na | na | na |
|  | B. Post-install average value | na | na | na | na | na | na | na | na | na | na |
| 6. Measure Count Data |  | NUMBER |  |  |  |  |  |  |  |  |  |
|  | A. Number of measures installed by participants in Part Group | Attached |  |  |  |  |  |  |  |  |  |
|  | B. Number of measures installed by all program participants in the 12 months of the program year | Attached |  |  |  |  |  |  |  |  |  |
|  | C. Number of measures installed by Comp Group | Attached |  |  |  |  |  |  |  |  |  |
| 7. Market Segment Data |  | SIC or CZ | PERCENT |  |  |  |  |  |  |  |  |
|  | Distribution by 3 digit SIC - Commercial/Industrial | See Attached |  |  |  |  |  |  |  |  |  |

| Southern California Edison |  |  |  |  |
| --- | --- | --- | --- | --- |
| M&E PROTOCOLS TABLE 6 - RESULTS USED TO SUPPORT PY96 SECOND EARNINGS CLAIM FOR |  |  |  |  |
| THE COMMERCIAL ENERGY MANAGEMENT HARDWARE REBATE PROGRAM |  |  |  |  |
| FIRST YEAR LOAD IMPACT EVALUATION, FEBRUARY 1998, STUDY ID NO. 540 |  |  |  |  |
| 6. Measure Count Data |  |  |  |  |
|  | Measure | A. Number of measures installed by participants in Part Group (n=269) | B. Number of measures installed by all program participants in the 12 months of the program year (n=775) | C. Number of measures installed by Comparison Group (n=308) |
|  | Air Compressor | - | 1 | - |
|  | Air Compressor System | - | 4 | - |
|  | Air distribution system | 48 | 48 | - |
|  | Anti-sweat heater | 225 | 418 | - |
|  | ASD (refrigeration) | - | 4 | - |
|  | ASD (space conditioning) | 85 | 156 | 1 |
|  | ASD (water services) | - | 4 | - |
|  | Chilled water controls | 1 | 1 | - |
|  | Chiller 200-600 ton | 1 | 3 | - |
|  | Chiller 75-200 ton |  | 2 | - |
|  | Component - air cooled single pkg AC | 46 | 85 | 1 |
|  | Component - disconnect lamp fixture rep | 6,665 | 7,486 | - |
|  | Component - disconnect lamp - rewire | 27,917 | 33,963 | 720 |
|  | Component - LED exit signs | 351 | 10,642 | - |
|  | Component - outdoor lght system mod | 1 | 244 | 324 |
|  | Component - outdoor lght system rep | 3 | 226,804 | 6 |
|  | Component - delamp from 8 to 4 ft | 168 | 6,700 | - |
|  | Component - delamp from fb40 to f17t8 | - | 1,574 | 788 |
|  | Cooling tower | - | 1 | - |
|  | Daylighting system | 48 | 48 | - |
|  | Economy cycle | 1 | 3 | - |
|  | EMS (lighting) | 19 | 87 | - |
|  | EMS (refrigeration) | - | 25 | - |
|  | EMS (space conditioning) | 9 | 90 | 3 |
|  | Indoor lght system - mod | 4,696 | 4,696 | - |
|  | Indoor lght system - rep | 84 | 87 | - |
|  | Misc (process) | - | 4 | - |
|  | Misc(refrigeration) | 6 | 7 | 1 |
|  | Misc (space conditioning) | 278 | 408 | - |
|  | Motors (HVAC) - 3 phase | - | 3 | - |
|  | Occupancy sensor - indoor | - | 12 | 4 |
|  | Pump system controls | - | 3 | - |
|  | Total | 40,652 | 293,613 | 1,848 |

| Southern California Edison |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M&E PROTOCOLS TABLE 6 - RESULTS USED TO SUPPORT PY96 SECOND EARNINGS CLAIM FOR |  |  |  |  |  |  |  |  |  |  |  |
| THE COMMERCIAL ENERGY MANAGEMENT HARDWARE REBATE PROGRAM |  |  |  |  |  |  |  |  |  |  |  |
| FIRST YEAR LOAD IMPACT EVALUATION, FEBRUARY 1998, STUDY ID NO. 540 |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | 7. Market Segment Data |  |  |  |  |  |  |  |
|  |  |  |  | B. Distribution of Participants by Industry (3-digit SIC) |  |  |  |  |  |  |  |
|  |  |  |  | 3-digit SIC | Percentage |  | 3-digit SIC | Percentage |  |  |  |
|  |  |  |  | 078 | 2.2 |  | 599 | 0.4 |  |  |  |
|  |  |  |  | 208 | 0.4 |  | 602 | 0.7 |  |  |  |
|  |  |  |  | 271 | 0.4 |  | 641 | 0.4 |  |  |  |
|  |  |  |  | 399 | 0.4 |  | 651 | 21.2 |  |  |  |
|  |  |  |  | 431 | 1.1 |  | 653 | 1.9 |  |  |  |
|  |  |  |  | 472 | 0.4 |  | 656 | 0.4 |  |  |  |
|  |  |  |  | 473 | 0.4 |  | 734 | 0.4 |  |  |  |
|  |  |  |  | 481 | 2.2 |  | 737 | 0.7 |  |  |  |
|  |  |  |  | 504 | 0.4 |  | 738 | 1.5 |  |  |  |
|  |  |  |  | 506 | 1.5 |  | 781 | 0.4 |  |  |  |
|  |  |  |  | 507 | 0.4 |  | 792 | 0.4 |  |  |  |
|  |  |  |  | 508 | 0.4 |  | 801 | 0.7 |  |  |  |
|  |  |  |  | 513 | 0.4 |  | 802 | 0.7 |  |  |  |
|  |  |  |  | 514 | 0.7 |  | 804 | 0.4 |  |  |  |
|  |  |  |  | 523 | 3.7 |  | 806 | 2.2 |  |  |  |
|  |  |  |  | 531 | 3.0 |  | 811 | 0.4 |  |  |  |
|  |  |  |  | 533 | 0.4 |  | 821 | 16.7 |  |  |  |
|  |  |  |  | 539 | 1.9 |  | 822 | 2.6 |  |  |  |
|  |  |  |  | 541 | 5.6 |  | 823 | 0.4 |  |  |  |
|  |  |  |  | 551 | 0.7 |  | 832 | 0.7 |  |  |  |
|  |  |  |  | 553 | 0.7 |  | 836 | 0.4 |  |  |  |
|  |  |  |  | 571 | 0.7 |  | 866 | 1.1 |  |  |  |
|  |  |  |  | 581 | 2.6 |  | 873 | 1.1 |  |  |  |
|  |  |  |  | 591 | 4.1 |  | 874 | 0.4 |  |  |  |
|  |  |  |  | 592 | 0.4 |  | 911 | 0.7 |  |  |  |
|  |  |  |  | 593 | 0.4 |  | 941 | 0.7 |  |  |  |
|  |  |  |  | 594 | 0.7 |  | 999 | 6.3 |  |  |  |

| Confidence Intervals |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 90% |  | t-stat | coefficient (see final model) | std.error (see final model) | Adj. % |  |  |
|  | ALL | 1.645 | 1 | 0.047 | 0.077315 |  |  |
|  | Lighting | 1.645 | 0.676472 | 0.03577179 | 0.086987 |  |  |
|  | HVAC | 1.645 | 1.031204 | 0.10777492 | 0.171925 |  |  |
|  | Refrigeration | 1.645 | 1.031204 | 0.10777492 | 0.171925 |  |  |
|  | Process | 1.645 |  |  |  |  |  |
|  | Miscellaneous | 1.645 |  |  |  |  |  |
| 80% |  | t-stat | coefficient (see final model) | std.error (see final model) | Adj. % |  |  |
|  | ALL | 1.282 | 1 | 0.047 | 0.060254 |  |  |
|  | Lighting | 1.282 | 0.676472 | 0.03577179 | 0.067792 |  |  |
|  | HVAC | 1.282 | 1.031204 | 0.10777492 | 0.133987 |  |  |
|  | Refrigeration | 1.282 | 1.031204 | 0.10777492 | 0.133987 |  |  |
|  | Process | 1.282 |  |  |  |  |  |
|  | Miscellaneous | 1.282 |  |  |  |  |  |
|  |  | Adj % = (Std.Error*t-stat)/coefficient |  |  |  |  |  |
|  |  | The upper bound values were computed as: |  |  |  |  |  |
|  |  |  | X+(X*adj %) |  |  |  |  |
|  |  | The lower bound values were computed as: |  |  |  |  |  |
|  |  |  | X-(X*adj %) |  |  |  |  |

# REPLACEMENT TABLES FOR THE TEXT OF THE STUDY

# Table 1:  Summary of Estimated Program Savings by End Use (kWh)

| Program Measure | SCE Gross Ex Ante Savings (kWh) | SCE Net Verified Savings (kWh) | RER Gross Realized Savings (kWh) | RER Net Realized Savings (kWh) |
| --- | --- | --- | --- | --- |
| Lighting |  |  |  |  |
| Indoor Ltg. | 22,079,125 |  | 17,147,470 | 13,635,918 |
| LED Ltg. Only | 2,612,422 |  | 2,612,422 | 1,800,063 |
| Outdoor Ltg. Only | 1,009,730 |  | 1,009,730 | 695,744 |
| Total Lighting | 25,701,277 | 17,677,140 | 20,769,622 | 16,131,726 |
| HVAC | 24,670,308 | 19,590,103 | 13,950,105 | 12,886,960 |
| Refrigeration | 3,245,731 | 2,484,264 | 2,179,294 | 2,179,294 |
| Process | 1,042,335 | 797,797 | 1,042,335 | 797,797 |
| Miscellaneous | 2,366,077 | 1,879,399 | 2,366,077 | 1,879,399 |
| All | 57,025,728 | 42,428,703 | 40,307,432 | 33,875,176 |

# Table 2:  Summary of Estimated Program Savings by End Use (kW)

| Program Measure | SCE Gross Ex Ante Savings (kW) | SCE Net Verified Savings (kW) | RER Gross Realized Savings (kW) | RER Net Realized Savings (kW) |
| --- | --- | --- | --- | --- |
| Lighting |  |  |  |  |
| Indoor Ltg. |  |  | 4,085 | 3,249 |
| LED Ltg. Only |  |  | 299 | 206 |
| Outdoor Ltg. Only |  |  | 8 | 6 |
| Total Lighting | 4,573 | 3,260 | 4,392 | 3,460 |
| HVAC | 685 | 563 | 1,785 | 1,649 |
| Refrigeration | 66 | 52 | 298 | 298 |
| Process | 108 | 85 | 108 | 85 |
| Miscellaneous | 22 | 18 | 22 | 18 |
| All | 5,453 | 3,978 | 6,605 | 5,510 |

# Table 1-1:  Summary of Estimated Program Savings by End Use (kWh)

| Program Measure | SCE Gross Ex Ante Savings (kWh) | SCE Net Verified Savings (kWh) | RER Gross Realized Savings (kWh) | RER Net Realized Savings (kWh) |
| --- | --- | --- | --- | --- |
| Lighting |  |  |  |  |
| Indoor Ltg. | 22,079,125 |  | 17,147,470 | 13,635,918 |
| LED Ltg. Only | 2,612,422 |  | 2,612,422 | 1,800,063 |
| Outdoor Ltg. Only | 1,009,730 |  | 1,009,730 | 695,744 |
| Total Lighting | 25,701,277 | 17,677,140 | 20,769,622 | 16,131,726 |
| HVAC | 24,670,308 | 19,590,103 | 13,950,105 | 12,886,960 |
| Refrigeration | 3,245,731 | 2,484,264 | 2,179,294 | 2,179,294 |
| Process | 1,042,335 | 797,797 | 1,042,335 | 797,797 |
| Miscellaneous | 2,366,077 | 1,879,399 | 2,366,077 | 1,879,399 |
| All | 57,025,728 | 42,428,703 | 40,307,432 | 33,875,176 |

# Table 1-2:  Summary of Estimated Program Savings by End Use (kW)

| Program Measure | SCE Gross Ex Ante Savings (kW) | SCE Net Verified Savings (kW) | RER Gross Realized Savings (kW) | RER Net Realized Savings (kW) |
| --- | --- | --- | --- | --- |
| Lighting |  |  |  |  |
| Indoor Ltg. |  |  | 4,085 | 3,249 |
| LED Ltg. Only |  |  | 299 | 206 |
| Outdoor Ltg. Only |  |  | 8 | 6 |
| Total Lighting | 4,573 | 3,260 | 4,392 | 3,460 |
| HVAC | 685 | 563 | 1,785 | 1,649 |
| Refrigeration | 66 | 52 | 298 | 298 |
| Process | 108 | 85 | 108 | 85 |
| Miscellaneous | 22 | 18 | 22 | 18 |
| All | 5,453 | 3,978 | 6,605 | 5,510 |

Table 4-5:  Gross Realized 96 EMHRP Program Demand Savings by End Use

| Program Measure | RER Gross Savings (kW) | Realization Rate | RER Gross Realized Savings (kW) | SCE ex ante Gross Savings (kW) |
| --- | --- | --- | --- | --- |
| Lighting |  |  |  |  |
| Indoor Ltg. | 6,008 | 0.68 | 4,085 |  |
| LED Ltg. Only | 299 | 1.00 | 299 |  |
| Outdoor Ltg. Only | 8 | 1.00 | 8 |  |
| Total Lighting | 6,315 |  | 4,392 | 4,573 |
| HVAC | 1,733 | 1.03 | 1,785 | 685 |
| Refrigeration | 289 | 1.03 | 298 | 66 |
| Process | 108 | 1.00 | 108 | 108 |
| Miscellaneous | 22 | 1.00 | 22 | 22 |
| All | 8,467 |  | 6,605 | 5,453 |

# Table 5-3: Net Realized Energy Savings

|  | SCE Estimates | RER Estimates |
| --- | --- | --- |
| End Use | Ex-Ante Gross Savings (kWh) | Net-to Gross Ratio* | Verified Net Savings (kWh) | Gross Realized Savings (kWh) | Overall Net-to Gross Ratio | Net Realized Savings (kWh) |
| Lighting |  |  |  |  |  |  |
| Indoor Ltg. | 22,079,125 |  |  | 17,147,470 | 0.795 | 13,635,918 |
| LED Ltg. Only | 2,612,422 |  |  | 2,612,422 | 0.689 | 1,800,063 |
| Outdoor Ltg. Only | 1,009,730 |  |  | 1,009,730 | 0.689 | 695,744 |
| Total Lighting | 25,701,277 | 0.689 | 17,677,140 | 20,769,622 | 0.777 | 16,131,726 |
| HVAC | 24,670,308 | 0.794 | 19,590,103 | 13,950,105 | 0.924 | 12,886,960 |
| Refrigeration | 3,245,731 | 0.765 | 2,484,264 | 2,179,294 | 1.000 | 2,179,294 |
| Process | 1,042,335 | 0.765 | 797,797 | 1,042,335 | 0.765 | 797,797 |
| Miscellaneous | 2,366,077 | 0.794 | 1,879,399 | 2,366,077 | 0.794 | 1,879,399 |
| Total Miscellaneous** | 6,654,143 | 0.777 | 5,161,460 | 5,587,706 | 0.869 | 4,856,490 |
| All | 57,025,728 | 0.744 | 42,428,7030 | 40,307,432 | 0.840 | 33,875,176 |

* SCE’s net-to-gross ratios include a verification factor of .957 .
** Total Miscellaneous includes refrigeration, process, and miscellaneous.

# Table 5-4:  Net Realized Demand Savings

|  | SCE Estimates | RER Estimates |
| --- | --- | --- |
| End Use | Ex-Ante Gross Savings (kW) | Net-to Gross Ratio | Verified Net Savings (kW) | Gross Realized Savings (kW) | Net-to Gross Ratio | Net Realized Savings (kW) |
| Lighting |  |  |  |  |  |  |
| Indoor Ltg. |  |  |  | 4,085 | 0.795 | 3,249 |
| LED Ltg. Only |  |  |  | 299 | 0.689 | 206 |
| Outdoor Ltg. Only |  |  |  | 8 | 0.689 | 6 |
| Total Lighting | 4,573 | 0.713 | 3,260 | 4,392 | 0.788 | 3,460 |
| HVAC | 685 | 0.822 | 563 | 1,785 | 0.924 | 1,649 |
| Refrigeration | 66 | 0.792 | 52 | 298 | 1.000 | 298 |
| Process | 108 | 0.792 | 85 | 108 | 0.792 | 85 |
| Miscellaneous | 22 | 0.822 | 18 | 22 | 0.822 | 18 |
| Total Miscellaneous** | 196 | 0.791 | 155 | 428 | 0.937 | 401 |
| All | 5,453 | 0.730 | 3,978 | 6,605 | 0.834 | 5,510 |

* SCE’s net-to-gross ratios include a verification factor of .990 .
** Total Miscellaneous includes refrigeration, process, and miscellaneous.

# Attachment C

Sent: 	Monday, May 04, 1998 4:54 PM

>To: 	Brown, Marian V

>Cc: 	Landry, Pierre H; Joshua Faulk

>Subject: 	Data Request #2 on Study 540

>

>I was making the following observation about an issue in my draft RM, and decided that this is something that can be quickly addressed, so as not to complicate the verification process, when the same question is likely to be asked.

>

>Page 4-4 says that the realization rate model is estimated with data

>covering both participants and nonparticipants, and under the third  bullet, the authors indicate that this date is very important for the model.  In addition, since it is a monthly model (building i in month t) the creation of a proper before and after period for the whole comparison group can be problematic. Presumably, the comparison group was not biased by eliminating cases that took no measures, and some dates were needed to determine the pre-post trend.  This study does not appear to discuss what decisions were made.

>

>Question:  Can you tell us how an installation date was chosen for the

>nonparticipants in the model who did not install anything during the period of analysis?

# Attachment D

# From:  Pierre Landry

Date: 	May 5, 1998

Ken, thanks for the chance to clarify that point so we don’t complicate the verification process.  I called Fred Sebold at Regional Economic Research and asked him to write up a brief explanation of how their model handled the situation described in your query.  Fred sent me back a reply within the hour, but unfortunately I couldn’t read it because of file format incompatability (something with which you have way too much familiarity).  It was at the end of the day, and the RER office was closed when I called back to get another version.

I just received the replacement copy this morning, and it should answer your questions.

_____________________________________________________________

Response:

There seems to be some confusion as to the use of the installation dates for measures.  These dates are used strictly to define the point at which some savings would be expected from an adopted measure.  An individual savings variable (let’s call it SAVit) is defined to be equal to 0 prior to the date of installation and equal to some engineering estimate after that date.  If a site adopts nothing, the value of SAVit is equal to 0 throughout the sample period.  This does not mean that the site was eliminated from the analysis.  It simply has its savings variables set equal to 0 for all periods.  (This just means that since it adopted nothing we expect no DSM savings.)

An example might help.  The following table indicates how a lighting savings variable would be constructed for three sites:

Site 1 adopted a lighting savings measure with an expected monthly savings of 500 kWh at the beginning of May, 1996;

Site 2 adopted an lighting measure expected to yield 200 kWh in monthly savings on July 1, 1996, then another measure that was expected to yield another 100 kWh on September 1; and

Site 3 adopting nothing.

Note that an individual site has installation dates for every adopted measure, and these dates are used to construct savings variables for all of the covered end uses.

# Example

Month	SAV1t  (Site 1)	SAV2t (Site 2)	SAV3t (Site 3)

Octber 1995	0	0	0

November 1995	0	0	0

December 1995	0	0	0

January 1996	0	0	0

February 1996	0	0	0

March 1996	0	0	0

April 1996	0	0	0

May 1996	500	0	0

June 1996	500	0	0

July 1996	500	200	0

August 1996	500	200	0

September 1996	500	300	0

October 1996	500	300	0

November 1996	500	300	0

December 1996	500	300	0

January 1997	500	300	0

And so on	500	300	0

_____________________________________________________________

Please let me know if you have any other questions, and I’ll see if I can get you answers.  And thanks again for the opportunity to clarify.

# Footnotes

See Attachment B to this Review Memo for documentation of the proper E-3 Table denominators for the realization rates. The realization rates reported in Table 6 (as revised in Attachment B of this Review Memo) is based on the load impacts found in the Study 540 for each of the non-miscellaneous end use elements, divided by the reconstructed E-3 Table for the first earnings claim.

See Attachment B to this Review Memo, question #3 and response.

See Attachment B to this Review Memo for documentation of the proper E-3 Table denominators for the realization rates. The realization rates reported in Table 6 (as revised in Attachment B of this Review Memo) is based on the load impacts found in the Study 540 for each of the non-miscellaneous end use elements, divided by the reconstructed E-3 Table for the first earnings claim.

Another potential issue was addressed in a data request and response:  see Attachments C & D to this Review Memo.